## Slide 1: Total Site Hydrogen Integration and Waste Hydrogen Purification for Minimising Fresh Hydrogen Consumption
Limei Gai*, Petar Sabev Varbanov, Yee Van Fan, Jiří Jaromír Klemeš
Sustainable Process Integration Laboratory – SPIL, NETME Centre, Faculty of Mechanical Engineering, Brno University of Technology - VUT BRNO, Technická 2896/2, 616 69 Brno, Czech Republic
III International Scientific Conference on “Sustainable and Efficient Use of Energy, Water and Natural Resources”, 19-24 April 2021 (Online)

## Slide 2: 1. Introduction
IEA, 2019, The Future of Hydrogen - Analysis and key findings. A report by the International Energy Agency. < https://www.iea.org/reports/the-future-of-hydrogen >

## Slide 3: Problems to be Solved
Lou Y, Liao Z, Sun J, Jiang B, Wang J, Yang Y. A novel two-step method to design inter-plant hydrogen network. Int J Hydrog Energy 2019;44:5686–95.
Ruan X, Huo W, Wang J, Guo M, Zheng W, Zou Y, et al. Multi-technique integration separation frameworks after steam reforming for coal-based hydrogen generation. Chin J Chem Eng 2020.
Purification C
Purification A
Plant B
Plant A
Purification B
Plant C
High-quality Fresh H2 (FR1)
Low-quality Fresh H2 (FRn)
Interplant H2 flow 1
Waste H2
Regenerated H2 with Purity 1
Regenerated H2 with Purity n
…
…
…
Waste H2 recovery/ regeneration System
Interplant H2 flow 2
Multiple-resource Total Site Hydrogen Integration with waste hydrogen recovery

## Slide 4: Aim and Novelty
    Novel Contributions:
    Integration and recovery of hydrogen in networks at Process and Total Site context
    Consideration of fresh H2 sources at different quality levels
    H2 PA is extended to Total Site scope and multiple fresh resources
    Sustainable waste H2 recovery design by techno-economic performance
Aim:
    Develop an extended Pinch Analysis (PA) to min fresh H2 consumption and max waste H2 recovery through Total Site Integration
    Consider various waste H2 purification options for the regeneration of waste H2 to further increase waste H2 recovery

## Slide 5: 2. Method
Overall integration procedure of multiple-resource Total Site Hydrogen Integration with waste hydrogen recovery
1. Data collection and extraction of H2 source and sink
2. Multiple-resource Pinch Analysis of intra-plant H2 network
3. Total Site H2 Integration of inter-plant H2 network with multiple-resource
4. Select and Simulate waste H2 purification process
5. Optimise the waste H2 recovery process by techno-economic analysis
6. Compare the old and new H2 Networks
Can waste H2 be purified?
Yes
No
Purified H2
End
Start

## Slide 6: Multiple-Resource Pinch Analysis of intra-Plant H2 Integration – Plants Alone
The order of utilisation of fresh H2 sources is FRn (lowest-quality fresh H2), FRn-1, ..., FR2, FR1 (highest-quality fresh H2)
The performed order of the Pinch points is FR1, FR2, ..., FRn
Wan Alwi SR, Manan ZA. Targeting Multiple Water Utilities Using Composite Curves. Ind Eng Chem Res 2007;46:5968–76.

## Slide 7: Multiple-resource Pinch Analysis of Total Site H2 Integration-I

## Slide 8: Multiple-resource Pinch Analysis of Total Site H2 Integration-II

## Slide 9: Optimisation of Waste H2 Purification
Objective: max total annual profit (TAP) | 
Constraints | 
Total product value: | 
Total annual capital cost | 
Annualisation factor: | 
Total operating cost: | 
Mass balance: | 
, , | 
H2 recovery ratio: | 
Objective: max total annual profit (TAP) | 
Constraints | 

## Slide 10: 3. Case study
Table 1. Hydrogen sources and sinks of hydrogen network in refineries
Lou Y, Liao Z, Sun J, Jiang B, Wang J, Yang Y. A novel two-step method to design inter-plant hydrogen network. Int J Hydrog Energy 2019;44:5686–95.
H2 network | H2 Sources | H2 concentration, vol% | Flowrate, kNm3/h | H2 Sinks | H2 concentration, vol% | Flowrate, kNm3/h
Plant A | SRA1 | 80 | 17.30 | SKA1 | 86.7 | 93.31
 | SRA2 | 80 | 60.68 | SKA2 | 83.6 | 82.66
 | SRA3 | 75 | 55.28 | SKA3 | 82.6 | 39.16
 | SRA4 | 75 | 25.87 | SKA4 | 74.9 | 12.47
 | SRA5 | 70 | 8.00 | SKA5 | 72.7 | 5.73
 | SRA6 | 65 | 3.84 |  |  | 
Plant B | SRB1 | 93 | 50.30 | SKB1 | 80.6 | 201.20
 | SRB2 | 80 | 33.53 | SKB2 | 78.9 | 14.53
 | SRB3 | 75 | 145.31 | SKB3 | 77.6 | 44.71
 | SRB4 | 75 | 11.12 | SKB4 | 75.1 | 58.12
 | SRB5 | 73 | 27.94 |  |  | 
 | SRB6 | 70 | 36.89 |  |  | 
Plant C | SRC1 | 98.3 | 3.23 | SKC1 | 99.9 | 9.68
 | SRC2 | 98.3 | 6.45 | SKC2 | 98.6 | 2.24
 | SRC3 | 97.5 | 6.45 | SKC3 | 97.5 | 11.29
 | SRC4 | 96 | 2.30 | SKC4 | 97 | 8.06
 | SRC5 | 95 | 6.45 | SKC5 | 90 | 12.10
 | SRC6 | 90 | 9.68 |  |  | 
 | SRC7 | 85 | 6.05 |  |  | 
First fresh H2 source (FR1-99.9%): fresh H2 with 99.9 % purity; Second fresh H2 source (FR2-95%): fresh H2 with 95 % purity

## Slide 11: Separation and Purification of Waste H2
Projects | Cryogenic | PSA | Membrane
Purity of recovered H2, mol% | 90-96 | > 99 | 90-98
Recycling ratio, % | 90-98 | 50-92 | 85-95
Feed H2 concentration, mol% | 15-75 | 75-90 | 15-90
Feed gas pressure, MPa | 0.5-7.5 | 1-4 | 1-16
Product H2 pressure, MPa | Feed pressure | Feed pressure | << Feed pressure
Pretreatment requirement | Very few | None | Remove CO2, H2S, etc
Capital cost | High | Medium | Low
Degree of easy expansion | Low | Medium | High
Operational reliability | Low | Medium | High
Equipment floor space | High | Medium | Low
Table 2. Comparison of waste H2 recovery technology in a refinery
Elsherif M, Manan ZA, Kamsah MZ. State-of-the-art of hydrogen management in refinery and industrial process plants. Journal of Natural Gas Science and Engineering. 2015;24:346-56.

## Slide 12
Organic porous mem.
Organic non-porous mem. (Molecular states)
High separation efficiency, complex principle
Screening principle
 | Glass mem. | Rubber mem.
H2 | 105 | 2.225
C1 | 1 | 2.9
C2= | 1.27 | 7.15
C2 | 0.25 | 8.25
C3= | 0.45 | 8.85
C3 | 0.06 | 10.25
C4+ | 0.05 | 17.4
N2 | 1.14 | 1
 | Glass mem. | Rubber mem.
H2 | 105 | 2.225
C1 | 1 | 2.9
C2= | 1.27 | 7.15
C2 | 0.25 | 8.25
C3= | 0.45 | 8.85
C3 | 0.06 | 10.25
C4+ | 0.05 | 17.4
N2 | 1.14 | 1
    Membrane Selection and Key Parameters
      Membrane separation performance
      Membrane separation coefficient: the ratio of two gases permeability rates
Rubber mem.
Glass mem.
Ruan X, Xiao H, Jiang X, Yan X, Dai Y, He G. Graphic synthesis method for multi-technique integration separation sequences of multi-input refinery gases. Sep Purif Technol 2019;214:187–95.

## Slide 13: 4. Results and Discussion
    Ideal target of Total Site Hydrogen Integration
    Identify cross-plant streams by revising the waste hydrogen discharge

## Slide 14: Multi-Resource Total Site H2 Integration
    Final solution of Multi-Resource Pinch Analysis of Total Site H2 Integration
      FR2-95% consumption reduced by 7.7 % (8.25 kNm3/h)
      Waste hydrogen discharge reduced by 21.3 % (8.25 kNm3/h)

## Slide 15: Multi-Resource Total Site H2 Integration

## Slide 16: Optimisation of Waste H2 Regeneration
Flowsheet of separation and purification process
    Waste H2 purification process by membrane separation
No membrane separation module in Aspen HYSYS
A membrane separation model is established by combining Component Splitter, Spreadsheet and Adjust function unit in Aspen HYSYS

## Slide 17: Process optimisation
(a) pressure vs membrane separation
    Optimise the separation and purification process
The influence of pressure on the waste hydrogen regeneration process
(b) pressure vs annual economic benefit

## Slide 18: Results: Economic Benefits
Table 6: Optimal results of each economic benefit
Payback Period: 3.2 mon. H2 recovery ratio: 95 %
FR2-95% reduced by 21.3 %; Waste H2 discharge reduced by 67.6 %
Projects |  | Load |  | Costs | 
Product Profit | Regenerated H2 | 1.81 | t/h | 39.51 | M€/y
 | Final waste H2 | 9.72 | kNm3/h | 10.11 | M€/y
 | Total Product Value |  |  | 49.62 | M€/y
Capital Cost | H2 membrane | 168 | m2 | 0.14 | M€
 | Compressor | 1.97 | MW | 3.21 | M€
 | Piping |  |  | 0.90 | M€
 | Total Capital Cost |  |  | 4.25 | M€
 | Total Annual Capital Cost |  |  | 0.56 | M€/y
Operating Cost | Feed of purification process | 30.4 | kNm3/h | 31.65 | M€/y
 | Power consumption | 1.97 | MW | 1.49 | M€/y
 | Total Operating Cost |  |  | 33.13 | M€/y
Total Annual Profit |  |  |  | 15.93 | M€/y

## Slide 19: 5. Conclusions
    Min FR2-95% consumption and min waste hydrogen discharge are reduced by 21.3 % and 67.6 %
    Presents significant economic benefits: total annual profit 15.93 M€/y, payback period 3.2 mon
    Visualised and simple, clear physical meaning and easy to understand
    Can also be applied to other Mass/Material Integration of inter-plant resource conservation network, e.g. water and CO2
    The effects of multiple contaminants
    Integration of hydrogen and work exchange networks with H2 pressure
Future Work

## Slide 20: Acknowledgment
    This research has been supported by the EU project “Sustainable Process Integration Laboratory – SPIL”, project No. CZ.02.1.01/0.0/0.0/15_003/0000456 funded by EU “CZ Operational Programme Research, Development and Education”, Priority 1: Strengthening capacity for quality research.

## Slide 21
1st public building in the world to use Thomas Edison’s electric lamps
1
24th Conference Process Integration, Modelling and Optimisation for Energy Saving and Pollution Reduction
Brno, Czech Republic
2nd Largest city of CZ
Historical Capital city in Moravia
31 October – 2 November 2021
City hall
Villa Tugendhat
Moravian Karst
City View
Mahen Theatre
Medlánky

## Slide 22
SPECIAL SESSION:
Integration of Smart Cities and Smart Industry for Circular Economy: Energy, Water and Waste to Secondary raw material for Sustainable Future
Invitation Code: sd21iscsi
Contact: fan@fme.vutbr.cz; varbanov@fme.vutbr.cz klemes@fme.vutbr.cz
Website: https://www.dubrovnik2021.sdewes.org/special-sessions
Deadline: Abstract (archival paper) December 15, 2020
Abstract (conference paper) August 30, 2021

## Slide 23: Thank you for your attention